## Slide 1
OBJECT FOLLOWING ROBOT USING ARDUINO UNO
MINI-PROJECT PRESENTATION
Department of Electronics and Communication Engineering Cooch Behar Government Engineering College Maulana Abul Kalam Azad University of Technology (MAKAUT)
PROJECT MEMBERS:
Anupam Dutta (34900323003) | Biraj Sarkar (34900323013) | Debanjan Chakraborty (34900323015) Sayan Sarkar (34900323048) | Soumyajit Pandit (34900323052)
PROJECT SUPERVISOR: Dr. Gautam Das

## Slide 2
Contents
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 1 of 11
01. INTRODUCTION & PROJECT OVERVIEW
Project motivations, HMI background, and active sensor envelope.
02. SYSTEM ARCHITECTURE DESIGN
Overall system block diagram and hardware pin connection mapping.
03. HARDWARE COMPONENTS & SENSORS
Arduino UNO board, HC-SR04, and IR proximity sensor modules.
04. ACTUATORS & MOTOR DRIVERS
Brushed DC BO geared motors and L298N H-Bridge driver module.
05. POWER SCHEME & SYSTEM STABILITY
Unified 7.4V battery pack delivery and power isolation details.
06. SOFTWARE CONTROL ALGORITHMS
State machine movements: forward, lateral turns, and search modes.
07. CONTROL SOFTWARE SOURCE CODE
Arduino C++ code implementation utilizing the NewPing library.
08. CALIBRATION & INTEGRATION
Sensor threshold calibrations and action-command state mappings.
09. PERFORMANCE TESTING & EVALUATION
Experimental ranging trials, system latency, and battery rtimes.
10. CONCLUSIONS & FUTURE SCOPE
Summary of prototype and solutions to auxiliary voltage drop resets.

## Slide 3
1. Introduction & Project Overview
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 2 of 11
Autonomous Target Following
Following capabilities represent an essential domain of Human-Machine Interaction (HMI). It enables hands-free operation and natural cooperation between humans and mobile platforms.
Active Sensory Envelopes
Traditional vision-based human tracking requires high processing power (like Raspberry Pi boards), increasing weight, cost, and power consumption. Acoustic and IR sensors offer a low-cost, power-efficient alternative.
Multi-Sensor System
By combining a front-mounted HC-SR04 ultrasonic distance sensor with side-mounted infrared proximity sensors, the robot establishes a clean spatial envelope to follow targets in real-time.
Real-World Applications
Highly applicable in industrial automation, smart hospital carts that follow medical staff, hands-free warehouse transport luggage, and automated shopping guides.

## Slide 4
2. System Architecture Design
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 3 of 11
Multi-Sensor Input Interface
An HC-SR04 ultrasonic sensor provides front distance metrics. Side-mounted left and right IR proximity sensors detect lateral offsets when the target moves sideways.
Central Processing Core
The Arduino UNO reads inputs, determines distance and target boundaries, and executes a state machine to compute direction and PWM motor speeds.
Differential Steering Actuation
The L298N H-Bridge motor driver regulates battery current to four BO geared motors. Steering is achieved by varying the rotation of left and right wheels.

## Slide 5
3. Arduino UNO & Sensors
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 4 of 11
Arduino UNO Development Board
Based on the ATmega328P microcontroller running at 16 MHz. Features 14 digital I/O pins (6 PWM) and 6 analog inputs. Runs the control loop that processes inputs and regulates actuators.
HC-SR04 Ultrasonic Distance Sensor
Measures target distance by transmitting 40 kHz acoustic waves. Ranging duration determines distance: d = (t * 0.034) / 2. Operates from 2 cm to 400 cm with a 3 mm accuracy.
Infrared Proximity Sensors
Dual side-mounted sensors detect lateral offset. Emits IR light; reflections decrease receiver photodiode resistance, outputting LOW when target is detected within 8 cm.

## Slide 6
4. Actuators & Motor Driver
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 5 of 11
L298N H-Bridge Motor Driver Module
Controls DC motor speed and direction using high-power transistors. Handles up to 2A per channel. Modulates average motor voltage via PWM signals on Enable pins (ENA, ENB).
Brushed DC BO Geared Motors
Four battery-operated (BO) geared motors operating between 3V and 9V. Features a 1:48 gear reduction ratio, providing 150 RPM at 6V with high torque.
4WD Kinematics & Steering Control
The motors are wired in parallel left and right pairs. Steering is achieved by differential speed: forward drive, reverse drive, and pivoting turns.

## Slide 7
5. Power Scheme & System Stability
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 6 of 11
Power Isolation & Split Rail Scheme
DC motors draw high starting currents, which drop the battery voltage and cause microcontroller resets. To prevent this, the power rails are separated. The 7.4V battery pack connects directly to the L298N driver, while the driver's onboard 5V regulator steps it down to power the Arduino UNO.
Microcontroller Resets and Brownouts
Initial prototype builds included a 0.96-inch SSD1306 OLED display and an SG90 micro servo motor. During active scans, the servo's high current load caused significant voltage drops (brownouts) on the 5V line, resetting the microcontroller and introducing sensor noise.
Stability Resolution
To ensure stable, reliable operation on a single battery power source, the OLED display and servo motor were excluded from the final deployed prototype. The grounds of the battery, Arduino, and motor driver are connected to establish a shared reference.

## Slide 8
6. Software Control Algorithms
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 7 of 11
Arduino Control Framework
Written in C++ using the Arduino IDE 2.x. Standard input/output pins are polled to drive state machine transitions. Incorporates the NewPing library for non-blocking acoustic ranging.
Closed-Loop State Transitions
Continually processes distance and lateral IR states. Triggers direction codes: Forward, Steer Left, Steer Right, Safe Recovery, and Search.
Calibration Limits & Speed Control
Maintains a safe follow envelope between 10 cm and 35 cm. Modulates motor PWM (170/220) dynamically based on distance to adjust speed.

## Slide 9
7. Control Firmware Source Code
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 8 of 11
Core loop() Structure
The main loop reads ultrasonic distance and flank IR sensors to trigger appropriate motor actions.
Safety Backup and Turn
If target is detected closer than 10 cm, the loop halts, reverses, turns right, and halts again to safely recover distance.
Target Searching
If target is lost or exceeds 35 cm, the robot pivots right to scan the surrounding area.
void loop() { int distance = sonar.ping_cm(); if (distance == 0) distance = 200; int rightIR = digitalRead(RIGHT_IR); int leftIR = digitalRead(LEFT_IR); analogWrite(ENA, (distance > 25) ? 220 : 170); analogWrite(ENB, (distance > 25) ? 220 : 170); if (distance < MIN_DISTANCE) { // Safety Stop & Backup setMotors('S'); delay(300); setMotors('B'); delay(400); setMotors('S'); delay(200); setMotors('R'); delay(300); setMotors('S'); return; } if (rightIR == LOW && leftIR == HIGH) setMotors('R'); else if (rightIR == HIGH && leftIR == LOW) setMotors('L'); else if (distance <= FOLLOW_DISTANCE) setMotors('F'); else setMotors('R'); // Search Mode }

## Slide 10
8. Calibration & Experimental Results
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 9 of 11
Sensor Threshold Configurations
IR sensors are adjusted using onboard potentiometers to ignore ambient lighting and trigger reliably at a maximum distance of 8 cm.
Command State Calibration Mapping
Calibration trials established solid tracking zones: - Under 10 cm: Safety Backup & Turn - 10 cm to 35 cm: Drive Forward - Over 35 cm: Target lost, enter Search pivot
Physical Platform Integration
All modules are integrated onto a 4-wheel acrylic chassis. Common grounding resolves electrical noise and signal fluctuations.

## Slide 11
9. Performance Testing & Evaluation
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 10 of 11
Tracking Reliability
Maintains a safe tracking boundary. Follows leading targets reliably between 10 cm and 35 cm without manual input.
Ranging & Latency Metrics
Ultrasonic sensor achieves accurate ranging with a variance of $\pm$0.5 cm. Low control loop latency (10 ms) enables real-time response to target speed shifts.
Power Runtime Capacity
Dual 18650 cells in series supply stable current for 50 minutes of continuous run time under full motor loads.

## Slide 12
10. Conclusions & Future Scope
OBJECT FOLLOWING ROBOT USING ARDUINO UNO | MINI-PROJECT PRESENTATION
Slide 11 of 11
Successful System Realization
Successfully built a low-cost, low-power autonomous Object Following Robot using the Arduino UNO microcontroller. The multi-sensor scheme tracks target objects or human subjects in real-time.
Cost-Effective Tracking
Showed that combining acoustic and infrared sensors provides a reliable tracking envelope, avoiding expensive and power-hungry computer vision processing boards.
Future Work & Enhancements
Planned expansions to enhance capabilities and resolve current prototype limitations: - Re-integrating the servo motor and OLED screen by adding an LM2596 buck converter to isolate electrical loads and prevent resets. - Upgrading the microcontroller to an ESP32 with an onboard camera (ESP32-CAM) for human recognition. - Implementing a PID control loop for smoother motor acceleration and deceleration curves.